## Slide 1: The Root of the DNS
Geoff Huston
APNIC
March 2017

## Slide 2: The Structure of the Domain Name Space
www.example.com.
. (“root”)
com.
example.com.
www.example.com.
Domain Names are a sequence of “labels” delimited by the period character that reflect a hierarchical name structure

## Slide 3: The Structure of the Domain Name System
The Domain Name System (DNS) is a distributed data collection using a delegation hierarchy that reflects the internal hierarchical structure of domain names. At each level in the name hierarchy each label represents a potential point of administrative delegation
www.example.com.
. (“root”) zone
com. zone
example.com. zone
www.example.com.
Each zone contains a list of defined labels
Labels can either reflect a delegation to a subordinate zone or they can be a terminal label that contains attribute information associated with that label
Delegation of the label “com”
Delegation of the label “example”
terminal label “www”

## Slide 4: Resolving a DNS Name
Your resolver needs need to ask a DNS server for the zone that contains the terminal label for the associated information (resource record) associated with the DNS name
But…
  Where exactly is the zone cut?
  Who are the servers?
So resolvers discover this information by performing a top-down iterative search…

## Slide 5: Resolving a DNS Name
Qname: www.example.com.?
. (“root”) zone server
Response: servers for the com. zone

## Slide 6: Resolving a DNS Name
Qname: www.example.com.?
. (“root”) zone server
com. zone server
Response: servers for the com. zone
Qname: www.example.com.?
Response: servers for the example.com. zone

## Slide 7: Resolving a DNS Name
Qname: www.example.com.?
. (“root”) zone server
com. zone server
example.com. zone server
www.example.com.
terminal label
Response: servers for the com. zone
Qname: www.example.com.?
Response: servers for the example.com. zone
Qname: www.example.com.?
Response: Resource records for terminal label

## Slide 8: How do we use the Root Service?
In the next few slides we’ll describe DNS behaviours and their use of the Root Service.
The DNS is full of variations in behaviour, and we can’t describe them all, so we’ll stick to what we observe as common behaviour here

## Slide 9: Every DNS Resolver starts up by asking a root server a priming query
Resolvers typically have a “hints” file to bootstrap into the DNS, but they use this to refresh the list of root name servers by asking one of the roots for the list of name servers for the root zone (the priming query)
Root Server Role: Answer priming queries about the root zone

## Slide 10: Every Name Resolution query starts by asking a root server

## Slide 11: Every Name Resolution query starts by asking a root server
In theory!
In practice, resolvers cache the responses they receive, and then use the cache for subsequent queries
This holds for the root zone as much as all other zones in the DNS, so in practice most queries for delegated domain names do not start with queries to the root zone

## Slide 12: Every DNS Resolver asks a root server about unknown names
DNS resolvers do not conventionally cache the entire root zone, but populate a local cache incrementally based on the names they are tasked with resolving
When a query cannot be answered from the local cache, the resolver will query a root server
Root Server Role: Answer cache miss queries from resolvers

## Slide 13: Root servers are promiscuous responders
Root servers do not “know” the reason for receiving a query, and have no policy about whether or not they should respond and with what information
Root servers respond using a common current copy of the root zone to form their response
Root Server Role: Answer all queries presented to root servers in a uniform and consistent manner based only on information in the root zone

## Slide 14: Root Service MUST be available
Not every root server needs to be reachable from every resolver that asks DNS queries, but at least one server must be available to respond to queries
If a resolver cannot reach ANY root servers then when its local cache expires it will be unable to answer queries. It will “go dark”
Root Server Role: The aggregate system of root servers must be available to respond to queries at all times

## Slide 15: Root Service needs to be ”fast enough”
An available Root Server should respond to queries in a timely manner
The faster the root server can respond the faster the overall DNS resolution time when the local resolver(s) have cache misses on the query, but there are no pre-defined target response times
Root Server Role: The aggregate system of root servers must respond to queries within a reasonable time

## Slide 16: Anycast Root Servers
12 of the 13 root server “letters” operate some form of “anycast” server constellation. All the servers in a constellation respond to the same public IP addresses. The routing system will direct resolvers to pass their query to a particular root letter to the “closest” member of the letter’s anycast constellation.
Anycast provides:
  faster responses to queries to the root for many DNS resolvers
  Greater resilience to hostile traffic by load sharing widely distributed attacks across the entire anycast constellation, and absorbing a single point attack on a single server instance

## Slide 17: Using the Root “Service”
The main role of the root server system is to answer queries that are not cached in local name caches
There are many more well-formed top level labels that are not delegated labels in the root zone than those that are (1,530)
That means that the vast majority of the queries that are passed to the root zone servers generate a “no-such-name” (NXDOMAIN) response from the root system

## Slide 18: Which Root?
There is no generic “any root server” address for a resolver to use. Resolvers need to send their queries to a specific letter.
Which letter they pick is up to the resolver. Some do round robin, some latch on to the one they think is faster. There are no particular rules that resolvers use here.
It’s not clear that resolvers use any particular heuristic to guide their choice of root server letter, nor is it clear that it matters in any case.
If there is no response, then the resolvers will switch to another root letter and repeat the query.

## Slide 19: Futures for the way we use the Root Service
As the traffic levels to the root servers increases both as steady state query levels and instances of attacks, we keep on building bigger servers and add more instances to the existing anycast clouds
Can we improve the behaviour of the total system to improve its overall scaling properties without singling out the root server system?

## Slide 20: DNSSEC changes Everything
Before DNSSEC we relied on the assumption that if we asked an IP address of a root server then the response was genuine
With DNSSEC we can ask anyone, and then use validation to assure ourselves that the answer is genuine
How can we use this?

## Slide 21: DNSSEC-Enabled Directions for the Root Service
DNSSEC opens some fascinating possibilities, allowing us to explore other options in how the root zone is distributed towards DNS resolvers in addition to the convention collection of Root Server Letter anycast constellations
The underlying ability provided by DNSSEC is that no matter how you obtain a response from the root zone, you can validate its authenticity with DNSSEC
This allows us to enlist DNSSEC-aware DNS resolvers to provide authoritative DNS responses from their local cache that would’ve otherwise required a query to a root server. This can be used to provide a significant augmentation to the capability of the root system without actually changing the scale or capability of the dedicated root zone servers themselves

## Slide 22: Local Root Secondaries - RFC7706
Enlist DNS resolvers to offer a root zone secondary service
If resolvers use this approach then they only need to query a root server infrequently and perform a zone transfer of the current state of the root zone (IXFR from a root server), and use this validated copy of the root zone to directly answer all queries that refer to the root zone

## Slide 23: “Aggressive” NSEC caching
Most of the queries seen at the root are for non-existent domains
Resolvers cache the nonexistence of a given name
But a DNSSEC-signed NXDOMAIN response from the root zone actually describes a range of labels that do not exist, and it’s the range that is signed, not the actual query name
If resolvers cached this range and the signed response, then they could use the same signed response to locally answer a query for any name that falls within the same label range
This has a similar effect to RFC7706, but without any configuration overhead, nor is there any requirement for supporting root zone transfers.
This approach increases the effectiveness of the local cache by allowing the local resolver to learn entire ranges of non-existent names in the root

## Slide 24: Research and Analysis
Can we peer inside the interactions between DNS resolvers and root servers to look at how the use the root system? Can we see to what extent resolvers spread their queries across the entire collection of root servers and to what extent they express a preference to use what they see as the “fastest” such server?
What is the interaction between V4 and V6 transports for the root servers and the anycast distributions?
What local caching parameters are used by DNS resolvers for root zone data?
To what extent do DNS resolvers ask for DNSSEC signatures for root zone data?

## Slide 25: Questions?